Water Supply

March/April 2000

Operations Group

March/April 2000

Operations Group

Review of Operations for the Period Ended 30 April 2000

### 1.	Items of Note

- Periods of heavy rain have resulted in minor problems at the treatment plants because of high river colour and turbidity.

2.	Water Quality

A total of 491 samples from trunk mains were tested for coliform organisms.  None of these samples tested positive.

Secchi disc water clarity in the Te Marua north lake varied between 5.4 m and 6.2 m, and in the south lake between 3.2 and 4.2 m.  These are considered satisfactory.  The dominant phytoplankton were as follows:

- North Lake:  Oscillatoria, Synedra, Chlorella

- South Lake:  Synedra, Staurastrum, and Peridinium

Oscillatoria is a filter clogging algae when present in high concentrations.

Synedra produces a musty smell and slick tongue sensation when abundant

Staurastrum produces a grassy smell when abundant.

Dissolved oxygen and pH readings are also satisfactory.

Giardia and Cryptosporidium results were as follows:

Te Marua

Lakes		)	No Giardia

)	No Cryptosporidium

Intake		)	No Giardia

)	No Cryptosporidium

Treated Water	)	No Giardia

)	No Cryptosporidium

Wainuiomata

Treated Water	)	No Giardia

)	No Cryptosporidium

Lower George Creek	)	No Giardia

)	Low Cryptosporidium

Big Huia Intake	)	Low Giardia

)	No Cryptosporidium

Intake		)	Low Giardia

)	Low Cryptosporidium

George Creek South arm	)	Low Giardia

)	Low Cryptosporidium

Orongorongo

Intake 		)	Low Giardia

)	Low Cryptosporidium

During March and April 2000 21 transgressions were notified:

- 5 low fluoride

- 9 low chlorine

- 1 high chlorine

- 1 low pH

- 1 presumptive coliform

- 1 high turbidity

- 2 high iron

3.	Supply Situation

The two monthly seasonal forecast for April and May 2000 issued by the Meteorological Service is as follows:

Situation as at 10 April:

For Wellington:

Rain: 			About normal

Wind: 			More southeast winds than normal

Temperature: 	Slightly below normal

Sunshine: 		About average

Specials:		Wet days from passing low pressure systems

Confidence: 		Moderate

Air temperatures are expected to be slightly below normal because the local sea surface temperatures have cooled recently.  Cold fronts are arriving about once a week, and are interspersed with find periods, but the sequencing in the pattern is becoming more jumbled as we move into autumn.  There may be some low pressure systems crossing central New Zealand from the Tasman Sea - keep an eye out for them, for they can bring the wettest day of the month.

Hutt River Flows

The mean monthly river flow for the month of March was slightly below average

Wainuiomata River Flows

Flow in the Wainuiomata River during March was average.

Aquifer Levels

The Waiwhetu aquifer level for March was above average.

4.	Production

4.1	Wainuiomata

4.1.1	Quality

- The polyelectrolyte supplier has changed their method of batching.  We have been trialing this since Easter and to date it has been successful.

- There have been several periods of heavy rain during which it was not feasible to run the treatment plant.

4.1.2	Safety

There are no accidents or incidents to report.

4.1.3	Operations

5 April:		The slam shut valve hydraulic ram seals started leaking.  The parts to carry out repairs are due to arrive on 5 May.  A two day shutdown is required to change the seals as soon as they arrive.

11 April:		The gatehouse valve failed to fully close, resulting in the treated water reservoir going empty.  The reservoir was slowly refilled but it still took 24 hours for the turbidity in the reservoir (from post-lime) to settle before the plant could be returned to service.

25 April:		The plant was off because of high river conditions.

27 April:		Commenced using different chemical suppliers for PAC.

4.1.4	Plant Tours

29 March: 		Wainuiomata School : 60 students

4.1.5	General

- While doing a full service on the air scour blowers, damage was identified in the blower vanes.  These have been sent for repair, with the first being repaired within three weeks.

- The standby PLC failed soon after being repaired.  Negotiations are being carried out with the supplier and repairer to solve the problem.

4.1.6	Projects

Capital Works

- The outlet flow meter installation has been postponed.  This will now be carried out on 9 May.

- The old Raroa Road flow meter from Karori is due to be installed on the Wainuiomata intake pipe.

Operational Projects

- The washwater recovery plant standby pump modifications are nearing completion.

- Work has started on reprogramming the PLC.

- The repositioning and final layout of the inlet monitoring instruments has begun.  These were temporarily moved to allow installation of the reaction tank.

4.2	Waterloo Water Treatment Plant

4.2.1	Quality

There are no quality issues to report.

4.2.2	Safety

There are no accidents or incidents to report.

4.2.3	Operations

- The Naenae flow meter has become erratic.  It is not responding to any of our efforts to correct the problem.  This meter has already been scheduled for replacement in June.

4.2.4	Plant Tours

There were no plant tours during the period.

4.2.5	Projects

Capital Works

- Considerable time has been spent on the System Optimisation project during this period.  This is currently on hold while a few issues are being resolved.

Operational Projects

- The refurbished Mahoe well pump has been recommissioned and is back in service.

- The next well pump refurbishment will commence in 1-2 weeks.

4.3	Gear Island

4.3.1	Quality

There are no quality issues to report.

4.3.2	Safety

There are no accidents or incidents to report.

4.3.3	Plant Tours

There were no tours during the period.

4.3.5	General

- Training is planned on the new DC drives and soft starter.

4.4	Te Marua

4.4.1	Quality

- Problems with the treatment process resulted in high aluminium levels in the treated water.   The plant outlet flow was diverted to Lake 1 until all filters had been backwashed and the treatment process reestablished.

4.4.2	Safety

An operator was stung by a wasp while assisting contractors involved in the pipe relining contract.  A wasp nest adjacent to where work was about to commence was located and destroyed by Wellington Regional Council staff.

4.4.3	Operations

2 March:		A filter sequence fault on filter 6 was caused by spider webs on the high level probes.

10 March:		Low treated water pH alarm caused by a sudden dip in the process signal.  No reason for the alarm was found.

12 March:		High treated water colour alarm caused by sample water blockage.

17 March:		Plant slam shut caused by power surge.

26 March:		High treated water colour alarm caused by spring failure on sample pump.

2 April:		Low plant air pressure caused by faulty refrigerant dryer.  The unit was bypassed and a service technician called in.

3, 6, 10 April:		High treated water turbidity alarm caused by grit being trapped in the sample cell.  A new turbidity instrument of different design is about to be installed and should eliminate similar problems in the future.

15, 29 April:		Filter 1 fault because of inlet penstock failure to open within the allotted time.  This problem also occurred in November 1999 and no cause could be identified.  Further investigation is underway but at this stage the problem has not been found.

4.4.4	Plant Tours

6 March:		St Joesph’s School : 110 people

8 March:		Otari Probus Club : 30 people

14 March:		South African group : 20 people

28 March:		Trentham School : 120 people

31 March:		Eastbourne Retired Persons’ Association : 30 people

10 April:		Hutt Combined Probus Club : 35 people

4.4.5	General

- The rotork actuator on the filter 6 outlet valve has been replaced with a spare.  The actuator became mechanically jammed and was unable to operate.  Repairs to the actuator are being carried out on-site and should be completed in early May.

- Kaitoke weir repairs have now been completed.  A close involvement by Te Marua staff was required to ensure the weir remained operational whenever possible.

- The Te Marua pipe relining contract was completed in late April.  Te Marua staff worked closely with the Engineering Consultancy Group and the Contractor as each section of pipe was isolated, drained and made safe.  Particular attention was paid to ensure all work undertaken complied with the Wellington Regional Council’s health and safety, and environmental procedures.

5.	Distribution

5.1	Electrical/Pipeline Sections

5.1.1	Flow Meters

- New electromagnetic flow meters have been installed at:

- Timberlea Reservoir inlet

- Mark Avenue Pumping Station, flow to Grenada South Zone

- The cable to the electromagnetic flow meter at Cruickshank was replaced after being damaged by rats.

5.1.2	ECNZ Reservoir, Haywards Hill

- A level transmitter and pressure bulb have been installed at the ECNZ reservoir at Haywards and the signal has been connected to the existing telemetry at Haywards Pumping Station.

5.1.3	Randwick Valve Chamber

- The No. 2 Pump has been removed and the mechanical seals replaced by a contractor and returned to service.

- The lighting, power circuits and rotten trunking have been replaced.

5.1.4	Hay Street Pumping Station

- The mechanical seals on No. 2 Pump have been replaced and the pump returned to service.

5.1.5	Thorndon Pumping Station

- A new pressure transmitter has been installed to measure the pressure in the Thorndon Zone.  It has been connected to the existing telemetry system.

6.	Health and Safety

Total Injury/Illness/Incident Record

Production

There was one incident involving an operator being stung by a wasp.

Distribution

One minor incident was reported on 31 March 2000, however there was no absence from work.

Network

One service person is off work because of a non-work related accident.

Operations Network

Review of Operations for the Period Ended 30 April 2000

### 1.	Items of Note

- During the period five burst mains were reported and all repaired within the allotted time frame.

### 2.	Water Supply (PT 30.1)

3.	Financial

### Facilities Management Contract Amounts - Wellington, including Tawa

| Month | Actual $ | Budget $ | Variance % | Year to Date | Budget $ | Variance % |
| --- | --- | --- | --- | --- | --- | --- |
| April | 219,067 | 294,314 | -25.57% | 2,278.806 | 2,943.140 | -22.57% |

### 4.	Water Quality

### 4.1	Routine Testing (PT 1.1)

The water quality was monitored and the appropriate laboratory tests were completed for April.  There were 136 samples from the reticulation system tested for bacteriological compliance.  Compliance for the month is 100 percent.  Compliance for the year to date is 100 percent.

### 4.2	Water Tests Initiated by Customers (PT 2)

|  |  | April | Year to Date | Compliance (%) Year to Date |
| --- | --- | --- | --- | --- |
|  | Number received | 7 | 86 | - |
| (PT 2.2) | Within ability of Operations Network to control | 0 | 16 | - |
| (PT 2.1) | Formal response within five days | 7 | 82 | 95% |

### 5.	Customer Services

### 5.1	Counter and Other Office Services (PTs 3.1, 4.1, 5.1)

Information has been provided to customers requesting information by letter, telephone and over the public counter.  A breakdown of enquiries received during the reporting period is as follows:

|  | April |
| --- | --- |
|  | Counter enquiries | 79 + 10 encroachments |
|  | Proposals from other utilities | 6 |
| (PT 33.1) | Plan records : New services recorded | 17 |
|  | Response time requirement compliance | 100% |

### 5.2	Complaints Register (Monthly Summary) (PT 5.1)

An enquiry/complaints register is being maintained.

A breakdown of complaints and enquiries received during the reporting period is as follows:

|  | April |
| --- | --- |
| (PT 2.2) | Water quality | 7 |
| (PT 16.1.2) | Pressure | 10 |
| (PT 20.1) | Reinstatement | 3 |
| (PT 16.1.4) | No-water | 9 |
|  | Contractors | 0 |
|  | Other | 0 |

All Water Quality complaints were responded to and completed within the performance criteria.  One of the 10 Pressure complaints was not attended to within the specified period, along with one of the No-water, which failed by three minutes.

### 6.	Response Maintenance

### 6.1	Compliance (PTs 9.1, 9.1a, 9.2, 10.1, 16.1)

|  | April |
| --- | --- |
|  |  | No. of Calls | Completed to Standard | Compliance % |
| (PT 9.1) | Stopcocks | 312 | 278 | 89 |
| (PT 9.1) | Hydrants | 114 | 100 | 88 |
| (PT 9.1a) | Valves | 27 | 13 | 48 |
| (PT 9.2) | Other leaks | 181 | 152 | 84 |
| (PT 10.1) | Mark-outs | 28 | 28 | 100 |
| (PT9.1a) | Value repacks | 27 | 17 | 63 |
| (PT 16.1.1) | Burst mains | 5 | 5 | 100 |
| (PT 2.1) | Water quality complaints | 7 | 7 | 100 |
|  |  | 701 | 600 | 86 |

Failures

|  | April |
| --- | --- |
|  | Jobs Failed by 1-24 Hours | Jobs Failed by 1-5 Working Days | Jobs Failed >5 Working Days |
| Fire hydrants | 3 | 6 | 5 |
| Mains | 0 | 2 | 0 |
| Valve repacks | 0 | 0 | 10 |
| Valves | 2 | 2 | 10 |
| Services | 7 | 10 | 10 |
| Tobies | 8 | 18 | 8 |
| Total | 20 | 38 | 43 |

Additional Work Carried Out

|  | April |
| --- | --- |
| New services | 30 |
| Damages by contractors | 18 |
| Variations | 6 |
| Renewals over 4 m | 2 |

### 6.2	Burst Mains (PT 16.1)

There were five burst mains during the month of April, these being as follows:

214 Oriental Parade	10 April 2000

214 Oriental Parade (second break)	10 April 2000

17 South Karori Road	16 April 2000

Cnr Franklyn Road and Hillary Street, Tawa	20 April 2000

9 Maurice Terrace, Lambton	27 April 2000

All of the burst mains were attended to within 30 minutes and repaired within eight hours.

### 6.3	Supply (PT 16.1)

|  | April |
| --- | --- |
| Total calls regarding loss or temporary loss of supply because of broken mains or supply failure | 9 |
| Total calls attended within 30 minutes | 8 |
| Total Compliance | 89% |

### 6.4	Reinstatement (PT 20.1)

There were three complaints received this month regarding trench reinstatements.  The Facilities Management Contract target is less than 12.

### 6.5	Shutdown Notification (PT 6.1)

There were 17 planned shutdowns during April.  All identifiable customers received notification within 24 hours prior to the shutdown.

### 6.6	Locates and Investigations (PT 10.1)

Work completed during the period comprised:

|  | April |
| --- | --- |
| Locate stopcocks | 73 |
| Leak location | 103 |
| Flow tests | 0 |
| Seepage/Investigations | 4 |
| Miscellaneous supply jobs | 1 |

### 7.	Health and Safety

There were no incidents reported this month, although one person is off work because of a non-work related injury.

### 8.	Meters (PT 13.1)

A total of 2,376 city, high use and voluntary meters were read, and entered into the system by 23 April 2000.

### 9.	Pumping Stations, Reservoirs and System Control

### 9.1	General

Normal routine maintenance has resulted in the Wellington City system operating satisfactorily.

### 9.2	Control System (PT 30.1)

The control system continues to operate satisfactorily.

### 9.3	Croydon Street Pumping Station

The No. 1 Pump has been replaced and recommissioned after being overhauled.

### 9.4	Burnside Pumping Station

Pump No. 2 has been installed and recommissioned after being overhauled.

### 9.5	New Flow Meters

New electromagnetic flow meters have been installed at:

- Thorndon to measure the total flow to the Low Level Zone

- Kelburn Reservoir inlet

- Maldive Regional Reservoir inlet

- Maldive Abattoir Reservoir inlet

### 9.6	Maintenance Checks (PT 17.4)

Maintenance has been carried out as follows:

| April |
| --- |
| Round C | Round D |
| Allington Road Messines Road Pumping Station Karori Park Montgomery Avenue Makara Road Verviers Street The Zoo Russell Terrace Lyndhurst/Chester Roads Mills Road Woodridge CV | Karepa Street Highbury Landfill Reservoir Landfill CV Rhine Street Beacon/Signal Hill Townsend Road Miramar North Dargle Way Grenada CV Rangoon Heights Ngaio CV |

### 10.	Development

### 10.1	Development Statistics

| Subdivisions | April | Year to Date |
| --- | --- | --- |
| Construction plans approved (lots/units) | 13 | 228 |
| Scheme plans approved | 36 | 304 |
| Subdivisions cleared (lots/units) | 42 | 493 |

### 10.2	Development Projects

10.2.1	Churton North Reservoir

The consultants are currently designing the electrical and control system, and preparing a chlorination procedure.  The first fill is expected soon, followed by the testing procedure.  The method of power (either solar/batteries or mains) is yet to be resolved.

10.2.2	Westchester Drive Pumping Station

The pumping station is complete.  Bracing struts have been installed to ensure the elevated pipework is stable during power failures.  The consultants are preparing a chlorination procedure for the station and rising main.  The consultants plan to switch on the station soon.  A noise test is being planned.

10.2.3	Hampton Gate, McLintock Street

The subdivider has agreed to pay for a changed method of control of the existing Broderick Road Pumping Station, the existing Johnsonville West Reservoir and the proposed Hampton Gate Reservoir.  The proposed Hampton Gate Reservoir will now be high enough to supply the subdivision with the required minimum Wellington City Council Code of Practice for Land Development pressures.  This issue has now been successfully resolved to the satisfaction of the Wellington City Council, the subdivider and Wellington Regional Council.  The resolution means that the Hearings Committee did not need to deal with this issue.

10.2.4	Major Subdivisions

Construction plans were submitted for approval of the following major subdivisions:

- 7-9 Hindmarsh Street, Johnsonville (7 lots).  This was approved on 4 April.

- De Bes Subdivision, Beacon Hill (5 lots).  This has not yet been finally approved, as we are waiting on information from the Wellington City Council.

- 252 Ohiro Road, Brooklyn (supply to 4 lots).  This has not yet been approved, as we have requested amended plans from the developer.

As-built plans were submitted for approval for the following major subdivisions:

- 12 Murray Street, Island Bay (2 lots).  This is not yet finally approved, as completion of outstanding work is awaited.

10.2.5	Fire Services Recently Connected (PT 12.1)

There were two fire services connected during the month.

- Maddison Gardens Rest Home, 11 Messines Road, Karori : 100 mm

- Parklane Apartments, 35 Johnston Street : 100 mm

10.2.6	New Commercial Metered Services

There were five new commercial metered services connected during the month:

- Maddison Gardens Rest Home, 11 Messines Road, Karori : 50 mm

- 28 Grey Street, Lambton : 50 mm

- Basin Reserve Road Gardens : 3 x 20 mm

### 10.3	Building Development Appraisals

|  | April |
| --- | --- |
|  | Commercial | Domestic |
| Building consents | 13 | 39 |
| PIMS applications | 13 | 40 |
| Compliance with response time requirement | 100% | 100% |

10.4	Land Information Memorandum

|  | April |
| --- | --- |
| Applications processed | 33 |
| Compliance with response time requirement | 100% |

### 11.	Capital Works

### 11.1	Main Laying : City

### 11.1.1	Contracts in Maintenance Period

The following pipelaying contracts in the central city are in the maintenance period:

- Manners Street

- Cuba Street

### 11.1.2	Taranaki Street

Contract Documents are being prepared for the replacement of the 150 mm cast iron and 150 mm asbestos cement mains in Taranaki Street.

### 11.2	Main Laying : Suburbs

### 11.2.1	Contracts in Maintenance Period

The following pipelaying contracts are in the maintenance period:

- Tirangi Road, McGregor, Kingsford Smith Street and George Bolt Streets

- Bracken Road

- Breaker Bay Road

- Makara Road Rising Main

- Owhiro Bay Parade

- Helston Road

- Rider Main Renewals

- Fox Street

### 11.2.2	Bell Road Zone Improvements

The Contractor, N Forsyth Ltd, is replacing the pipes in Salisbury Terrace and Salisbury Avenue.  The Contractor is about to start on Bidwill Street and then move on to Rolleston Street.

### 11.3	High Level Distribution and Storage

### 11.3.1	Karori South and Allington Road Zones Amalgamation

Tenders have been invited to install a pipeline to link the Karori South and Allington Road water supply zones.

### 11.3.2	Wadestown Reservoir

The consultant is progressing the design and preparation of Contract Documents. Agreement has been reached with Telecom New Zealand Ltd to allow access across their land for construction traffic.

### 11.3.3	Grenada North High Level Reservoir

Draft Contract Documents have been received from the consultant.  These have been reviewed and comments provided.

The resource consent for the construction of the reservoir is about to be issued.

### 11.4	Low Level Zone Storage

11.4.1	Eastern Suburbs Reservoir

A report on the preliminary assessment of the potential reservoir sites is being prepared.

| Analysis - December 1998 to April 2000 |
| --- |
|  | Quality Reports PT 2.1 | No of Planned Shut-downs PT 6.1 | Stopcocks PT 9.1 | Leaking Hydrants PT 9.1 | Leaking Valves PT 9.1a | Leaks PT 9.2 | Mark-outs PT 10.1 |
|  | Calls Received | 5 Day Response | % Compl. | Completed | Calls Received | Completed | % Compl. |  | % Compl. |  | % Compl. | Calls Received | Completed | % Compl. | Received | % Compl. |
| July 1998 | 8 | 8/8 | 100% | 2 | 371 | 359 | 96% | 90 | 94% | 24 | 100% | 231 | 213 | 95% | 61 | 95% |
| August 1998 | 10 | 17/18 | 94% | 2 | 304 | 243 | 87% | 91 | 86% | 25 | 100% | 216 | 183 | 85% | 74 | 100% |
| September 1998 | 11 | 26/29 | 90% | 4 | 289 | 211 | 81% | 71 | 77% | 13 | 100% | 219 | 183 | 84% | 74 | 100% |
| October 1998 | 6 | 32/35 | 91% | 3 | 385 | 293 | 73% | 107 | 73% | 6 | 100% | 216 | 147 | 68% | 67 | 100% |
| November 1998 | 7 | 37/42 | 88% | 3 | 421 | 382 | 76% | 70 | 75% | 13 | 100% | 228 | 198 | 86% | 91 | 100% |
| December 1998 | 9 | 46/51 | 92% | 2 | 365 | 362 | 90% | 79 | 78% | 9 | 100% | 234 | 233 | 99% | 16 | 100% |
| January 1999 | 13 | 59/64 | 93% | 25 | 431 | 429 | 99% | 77 | 64% | 15 | 93% | 275 | 271 | 98% | 21 | 100% |
| February 1999 | 10 | 69/74 | 93% | 30 | 343 | 336 | 97% | 106 | 81% | 18 | 94% | 176 | 170 | 96% | 11 | 100% |
| March 1999 | 5 | 74/79 | 94% | 34 | 488 | 359 | 74% | 118 | 94% | 12 | 92% | 324 | 282 | 84% | 108 | 100% |
| April 1999 | 5 | 79/84 | 94% | 18 | 430 | 367 | 85% | 129 | 91% | 20 | 95% | 259 | 221 | 85% | 94 | 100% |
| May 1999 | 8 | 86/92 | 93% | 18 | 366 | 285 | 78% | 110 | 78% | 10 | 80% | 239 | 200 | 84% | 140 | 100% |
| June 1999 | 5 | 90/97 | 93% | 18 | 364 | 269 | 74% | 90 | 68% | 21 | 95% | 262 | 204 | 77% | 86 | 100% |
| Summary (1998/9) | 97 | 90/97 | 93% | 159 | 4557 | 3915 | 86% | 1138 | 81% | 186 | 96% | 2879 | 2505 | 87% | 823 | 99% |
| July 1999 | 16 | 15/16 | 94% | 18 | 385 | 345 | 92% | 72/78 | 92% | 18/19 | 95% | 267 | 258 | 96% | 47 | 100% |
| August 1999 | 6 | 6/6 | 100% | 15 | 347 | 333 | 91% | 85/89 | 96% | 16/19 | 84% | 241 | 225 | 98% | 51 | 100% |
| September 1999 | 1 | 1/1 | 100% | 12 | 356 | 275 | 82% | 68/72 | 94% | 18/20 | 90% | 276 | 226 | 82% | 41 | 100% |
| October 1999 | 13 | 13/13 | 100% | 21 | 320 | 241 | 75% | 71/87 | 81% | 19/20 | 95% | 234 | 198 | 85% | 40 | 100% |
| November 1999 | 12 | 12/12 | 100% | 16 | 365 | 334 | 92% | 81/92 | 88% | 11/13 | 85% | 246 | 228 | 93% | 30 | 100% |
| December 1999 | 4 | 4/4 | 100% | 8 | 364 | 346 | 95% | 77/80 | 96% | 21/32 | 66% | 218 | 194 | 89% | 28 | 100% |
| January 2000 | 3 | 3/3 | 100% | 0 | 391 | 341 | 87% | 77/94 | 82% | 18/26 | 69% | 237 | 182 | 77% | 40 | 100% |
| February 2000 | 9 | 7/9 | 78% | 6 | 467 | 389 | 83% | 102/117 | 87% | 19/25 | 76% | 222 | 196 | 88% | 57 | 100% |
| March 2000 | 15 | 14/15 | 93% | 46 | 473 | 405 | 86% | 105/134 | 78% | 14/17 | 82% | 247 | 204 | 83 | 24 | 100% |
| April 2000 | 7 | 7/7 | 100% | 17 | 312 | 278 | 89% | 100/114 | 88% | 13/27 | 48% | 181 | 152 | 84% | 28 | 100% |
| Running Total for Current Year | 86 | 82/86 | 95% | 159 | 3,780 | 3,287 | 87% | 838/976 | 86% | 167/218 | 77% | 2,369 | 2,063 | 87% | 386 | 100% |
| Analysis - December 1998 to April 2000 |
|  | Loss of Supply PT 16.1 | Burst Mains PT 16.11 | Reinstatements PT 20.1 | Toby Locates | Damage Repairs | Total Calls |
|  | Complaints Received | % Compl. | Occurred | % Compl. | Occurred | % Compl. |  |  | Calls Received | Completed | % Compl. |
| July 1998 | 29 | 97% | 6 | 100% | 3 | 100% | 81 | 91 | 791 | 753 | 95% |
| August 1998 | 31 | 97% | 2 | 100% | 4 | 100% | 89 | 100 | 703 | 613 | 81% |
| September 1998 | 30 | 100% | 8 | 100% | 1 | 100% | 97 | 98 | 683 | 553 | 81% |
| October 1998 | 29 | 83% | 5 | 100% | 0 | 100% | 72 | 57 | 795 | 605 | 76% |
| November 1998 | 24 | 96% | 9 | 90% | 3 | 100% | 89 | 103 | 838 | 751 | 90% |
| December 1998 | 15 | 80% | 4 | 100% | 1 | 100% | 101 | 26 | 770 | 763 | 99% |
| January 1999 | 21 | 100% | 7 | 100% | 1 | 100% | 92 | 23 | 875 | 868 | 99% |
| February 1999 | 25 | 96% | 5 | 100% | 0 | 100% | 100 | 29 | 647 | 630 | 97% |
| March 1999 | 32 | 97% | 8 | 100% | 0 | 100% | 102 | 102 | 1073 | 884 | 82% |
| April 1999 | 46 | 94% | 7 | 100% | 1 | 100% | 64 | 46 | 945 | 831 | 88% |
| May 1999 | 32 | 100% | 2 | 100% | 1 | 100% | 81 | 109 | 875 | 729 | 83% |
| June 1999 | 33 | 85% | 7 | 100% | 3 | 100% | 80 | 105 | 837 | 655 | 78% |
| Summary (1998/9) | 347 | 94% | 70 | 99% | 18 | 100% | 1048 | 889 | 9832 | 8635 | 88% |
| July1999 | 19/22 | 86% | 8 | 100% | 4 | 100% | 91 | 75 | 830 | 767 | 92% |
| August 1999 | 14/16 | 88% | 9 | 100% | 0 | 100% | 85 | 34 | 807 | 735 | 91% |
| September 1999 | 50/50 | 100% | 9 | 100% | 1 | 100% | 75 | 54 | 777 | 640 | 82% |
| October 1999 | 17/17 | 100% | 4 | 75% | 0 | 100% | 76 | 22 | 724 | 591 | 82% |
| November 1999 | 9/10 | 90% | 8 | 100% | 1 | 100% | 72 | 29 | 774 | 709 | 92% |
| December 1999 | 23/23 | 100% | 5 | 100% | 1 | 100% | 64 | 20 | 744 | 681 | 92% |
| January 2000 | 3/4 | 75% | 7 | 100% | 0 | 100% | 83 | 16 | 809 | 677 | 84% |
| February 2000 | 2/2 | 100% | 5 | 100% | 0 | 100% | 135 | 58 | 909 | 783 | 87% |
| March 2000 | 8/8 | 100% | 4 | 100% | 0 | 100% | 113 | 41 | 929 | 782 | 84% |
| April 2000 | 8/9 | 89% | 5 | 100% | 3 | 100% | 73 | 18 | 703 | 602 | 86% |
| Running Total for Current Year | 153/160 | 96% | 64 | 98% | 7 | 100% | 867 | 367 | 8,006 | 6,967 | 87% |

Strategy and Asset Group

March/April 2000

Strategy and Asset Group

Review of Operations for the Period Ended 30 April 2000

### 1.	Items of Note

- The Hutt City and Wellington Regional Councils have resolved the non-fluoridation of the Petone water supply issue.  A formal agreement is to be prepared.  In the meantime sufficient funds have been allocated to allow detailed design work to start for changes to the water supply system and a works programme prepared.

- The MITS Hansen asset management system is a major advance on the previous paper based systems.  The depreciation module is being commissioned at present in conjunction with the Finance Department.

- A meeting was held with a supplier of membrane filtration equipment.  This was in regard to possible use in the waste water recovery plant system at the Wainuiomata Water Treatment Plant.  Membranes are still reducing in price and now appear to be comparable in price to conventional water treatment, such as clarification and filtration.  Their advantage is the ability to remove all particles except 1 in 1,000,000 (six log removal) of Giardia/Cryptosporidium size compared to about 1 in 1,000 (three log removal) for a conventional water treatment plant.  Watercare has chosen a membrane system for their Waikato River supply source.  The supplier is undertaking some preliminary design work at no cost to The Water Group.

- A satisfactory private binding ruling has been received from the Inland Revenue Department regarding the Karori land transfer.  Survey work to create the various land titles will start shortly.

- A separate report on the Public Perception of Water Quality has taken some time to produce over the past month.

### 2.	Sales Volume : Water Consumed from 1 April to 30 April 2000

- There is a marginal difference in consumption over the same period last year.  Given that a number of new water meters have been installed since last year, a slightly greater consumption for this year, compared to last, would have been expected.

3.	Asset Management

- The Revaluation of Wholesale Water Assets has been completed, the values loaded into a trial database and book values calculated to 30 June 1999 using the Hansen valuation module.  This work has been done using a trial database but no problems have been experienced.  Details of how the ongoing financial management of assets at a component level can be interfaced with the SAP financial system are being developed in consultation with the Finance Department.

- A review of the June 1998 Asset Management Plan has commenced but no significant changes will be made until the 2000/01 financial year.

- Capital works for 1999/00 are progressing.  Cement mortar lining of the wholesale water mains at Te Marua has been completed.  Commissioning of stage 1 of the System Optimiser is partially complete.  The complexity of the Wainuiomata/Waterloo supply system has extended the commissioning period beyond that anticipated.  The System Optimiser will select water sources and manage pump use to minimise the cost of the production and distribution of water.

The projected full year expenditure on capital works for 1999/00 is $4.017 m against a budget of $4.165 m.  Of this amount, $400,000 will be rebudgeted to 2000/01 to complete projects that have been delayed.

- A resource consent application for a new well tapping the Moera aquifer at Gear Island is being prepared.  A new well may affect IBM’s firefighting wells.  To check this, tests on the IBM well have been arranged.  An investigation bore being drilled into the Moera aquifer near Ewen Bridge by the Resource Investigations Section is currently being tested.

- Applications and environmental assessments for new surface water take consents have been prepared.  Details of the content and significance of these applications are reported separately.

- A resource consent to discharge supernatant into the Wainuiomata River intermittently has been granted.  The consent allows discharge of supernatant to the Wainuiomata River for approximately 30 percent of the time under defined conditions.  Recycling of the remainder of the supernatant is proposed but is dependent on the approval of the Public Health Authorities.  They have requested preparation of a Protozoa Risk Management Plan and this is in underway.  In the meantime the new consent cannot be implemented.

- Detailed seismic review and risk assessment work has been carried out for a number of network elements.  These reports have been reviewed and summarised, and a programme of proposed strengthening and remedial works is being compiled.

- A draft Risk Policy, which will provide broad guidelines for the management of risks to the water business, has been prepared.  It will be presented to the June Utility Services Committee meeting.

- Animal culling in the Wainuiomata/Orongorongo Catchment using balloted amateur hunters has been completed.  Modest success has been achieved, with 12 deer, 11 pigs and 11 goats being shot.  A more detailed report will be available at a later date.

- Seven disused wells adjacent to the old Hutt Park Pumping Station were recently sealed.  These wells have been unused and represented a threat to the aquifer.

4.	Quality Assurance

- Statistical analyses of turbidity readings to demonstrate compliance with the rule that requires turbidity to be less than 0.5 NTU for 95 percent of the time have been carried out.  The results for March and April are set out below.  The percentage of the time turbidity is less than 0.1 NTU has also been calculated.

| Percentage Compliance | Turbidity <0.5 NTU | Turbidity <0.1 NTU |
| --- | --- | --- |
| Plant | March | April | March | April |
| Te Marua | 99.98 | 99.98 | 99.66 | 99.96 |
| Wainuiomata | 100.00 | 99.98 | 93.59 | 75.71 |

The >0.2 NTU change within 10 minutes rule has been tested for Wainuiomata Water Treatment Plant.  This rule identifies “spikes” in the turbidity results, which have the potential to carry protozoa into the treated water.  The results are as follows:

| No. of Exceedances |
| --- |
| Plant | January | February | March | April |
| Wainuiomata | 10 | 2 | 3 | 16 |

This criterion has not been analysed for Te Marua, as the turbidity is monitored downstream of the treated water reservoir.  This reservoir masks any “spiking” through the filters.

Reasons for the high number of occurrences in April are being investigated.

These rules are intended to reduce the risk of Giardia and Cryptosporidium passing through the plant.  The plants incorporate “slam shut” valves so that any water that does not comply with the 0.5 NTU rule is not delivered to the customers.

- Work is continuing on the proposed Environmental Management System being developed under the provisions of ISO 14001.  An initial document audit was carried out by international accreditation agency BVQI on 21 March.  The auditor raised a number of issues and these are currently being addressed.

The final certification audit is scheduled for 19 June.

5.	Marketing

5.1	Market Research : Summer Water Conservation Campaign

- Research was undertaken to gauge the effectiveness of Wellington Regional Council’s summer water conservation campaign.  Interviewing was carried out during March, with data tables and an executive summary delivered by Colmar Brunton Research in mid-April.  A detailed analysis of the results is well advanced.  Individual presentations will be made to customers and full details will be reported to the Committee in June.  The “top line” result shows 64 percent of all people and up to 77 percent of main target groups recalled seeing our television commercial featuring Maggie Barry.

5.2	Summer Water Supply Analysis

- An analysis of water supply volumes, sunshine hours and rainfall volume and patterns was completed for the three month period December 1999 to February 2000.  This analysis provides an explanation for the modest demand levels experienced during summary 1999/00 compared with the previous year.  A copy of this analysis was provided to Councillors, customers and staff with issue 71 (March 2000) of Water Watch.

5.3	Internet

- Continuation of a full review of structure and content of the Water Supply section of the Wellington Regional Council Internet site.  Further changes to the text and graphics were written/sourced.  These changes are now with Information Technology for incorporation into the live site.  Links to all background documents on the live site have been updated previously.

- Our Information Technology Department reports that for the two week period 14-27 March there were 89 visitors to the Water Supply pages of the site and 41 to the Wonderful Water educational resource.  This result compares well with other division-specific areas of the Wellington Regional Council site.

- The editor of the Los Angeles Times web site considered our Water Supply pages worth linking their site to as part of a water supply educational profile.  This resulted in 34 hits on our site over a two week period in April.

5.4	Other Activities

- A paper entitled Water Supply - Contributing to the Greater Public Good was completed for David Benham, Divisional Manager, Utility Services.

- A media release Thorndon roadworks herald new water meter for Wellington was written and released on 27 March.

- Arrangements commenced for the Utility Services Division’s involvement in the Upper Hutt Science Festival, a programme to promote the role of science in the community.  An open day at Te Marua involving presentations and a guided tour is being planned for Saturday, 22 July, in conjunction with the Operations Group and Laboratory Services.

- Work progressed in conjunction with the Environment Division’s Learnwell programme being developed for water conservation.  This will address Utility Services’ objectives for educational material, as well as the Environment Division’s.

5.5	Economics

- The new wholesale water database has now been running for approximately seven months.  Minor teething problems have been fixed and an instruction manual compiled.  An automated reporting process is being advanced.

- A time dependent database package suitable for the storage of data from the telemetry system has been selected and is currently being evaluated.

- A new contract for the supply of electricity was negotiated between the Council and TrustPower, and was implemented in October 1999.  In-depth analysis is currently being done in conjunction with implementation of the pumping station optimiser to try and minimise costs.

- The 1999 benchmarking report is now finished.

6.	Projects Undertaken by Engineering Consultancy for the Strategy and Asset Group

- Te Marua Lakes to Treatment Plant Pipelines

The cement mortar lining Contract attained Practical Completion on 1 May 2000.  This Contract is now in the maintenance period.

- Kaitoke Weir Repair

The Contract for repairing the Kaitoke Weir attained Practical Completion on 29 March 2000 and is now in maintenance.  Additional minor repair work is proposed during the low river flow period next summer.

- Kaitoke Concrete Pipeline

Repair works to the joints on the concrete pipeline between the Kaitoke Flume Bridge and the No. 2 Tunnel entrance are proposed.

Details of suitable materials for this work are being obtained from the suppliers.

- Branch Line to Plateau Reservoir

Upper Hutt City Council has requested a direct connection from the Kaitoke main to the Plateau Reservoir at Te Marua.  A design report for this pipeline has been prepared.

- Silverstream Scour on Kaitoke Main

A drawing detailing a new connection and scour for the Kaitoke main at Silverstream has been prepared.

- OK Main Slip Lining : Waiapu Road to The Rigi

The Contract for slip lining the OK main between The Rigi and Waiapu Road is in maintenance.

- OK Main Cement Mortar Lining : Thorndon to Karori

The Contract Documents for the cement mortar lining of the OK main between Thorndon and Karori are being prepared.

- OK Main Crossing of Korokoro Stream

The OK main between Randwick and Korokoro supplies water to the new Rahui Reservoir.  The pipe crossing the Korokoro Stream is corroded and poorly supported.  A design report recommending the method of replacement has been prepared.

###### Plimmerton/Pukerua Bay Branch Pipeline Shut-off Valve

The valve chamber and shut-off valve have been installed.  Arrangements are being made to commission the automatic control of the valve.

- Hutt Estuary Bridge Pipelines

Quotations have been received for the supply of flexible couplings for our pipelines on the Hutt Estuary Bridge to accommodate the design movement of the bridge in a seismic event.  These quotations are being assessed.

- Buick Street Pumping Station Decommissioning

Arrangements are being made to plug the bores and remove the pumping station building.  This work is programmed for May/mid-June 2000.

###### Wainuiomata River Bridge

The Wainuiomata River Bridge strengthening project is complete.

#### Karori Reservoir Rationalisation

All major pipework alterations are complete and the site has been cleaned up.  A number of minor outstanding items are being attended to.

- Haywards Reservoir Utilisation

New control valves and pipework are proposed for Haywards Reservoir.  This is to allow remote control, turnover in the reservoir to maintain water quality and greater utilisation of the available water storage.  Construction drawings have been issued and work is about to start on-site.

- Water Meter Replacement Programme

The programme of replacing the existing revenue meters is progressing satisfactorily.  Fourteen meters have so far been installed this financial year.  Four more meters are programmed to be installed by the end of June 2000.

- Te Marua Lakes Surveillance Manual

The condition of the Te Marua Lakes’ embankments and structures is regularly monitored.  The monitoring procedures are detailed in the Te Marua Lakes Surveillance Manual.  The manual was initially produced in 1989.  The manual is being updated to take into account changes in monitoring requirements and changes in the Wellington Regional Council structure.

Engineering Consultancy Group

March/April 2000

Engineering Consultancy Group

Review of Operations for the Period Ended 30 April 2000

1.	Work Carried Out for the Strategy and Asset Group

The main capital projects for which the Engineering Consultancy Group has responsibility are itemised in the Strategy and Asset Group report.  Support is also provided for other projects being undertaken by this group.

2.	Work carried Out for the Operations Group

The Engineering Consultancy Group has continued to provide support for smaller projects arising from the operation and maintenance of the wholesale water supply system.

3.	Work carried Out for Wellington City Council

3.1	General

Current projects underway are detailed in the following sections.

3.2	Pipeline Projects

Contracts were completed for the replacement of water mains for two difficult inner city projects.  These are Manners Street, from Cuba to Willis Street, and Cuba Street, from Ghuznee to Webb Street.

Tenders were invited and a Contract awarded for main laying in Rolleston Street, Salisbury Avenue, Salisbury Terrace and adjustment to the Bell Road Zone.  This work is about to commence and will resolve a longstanding low pressure problem in this area.

Contract Documents are being prepared for a replacement main to be laid in Taranaki Street from Courtenay Place to Webb Street.  This will be difficult because of the extensive underground services, as well as the constraints arising from the route being on State Highway.

3.3	Grenada North High Level Reservoir

This permanent reservoir, 150 m³ capacity, will replace the Grenada North temporary tanks.  The site is at a higher level to the east of Nassau Avenue on land that has recently been transferred from TransPower to Wellington City Council.  The intention of this reservoir and associated pipework is the second stage in the upgrade of the Grenada North water supply following the contamination incident in early 1998.

Work is proceeding on the preparation of the plans and Contract Documents.

3.4	Wadestown Reservoir

Montgomery Watson Ltd was engaged for the design of a replacement reservoir, capacity 1,800 m³, along with the obtaining of resource consents necessary for the completion of the reservoir on the Town Belt, as well as for access across the Town Belt.

Agreement has been reached with Telecom New Zealand Ltd to allow access to the site from Northland.  A change has been made to the reservoir dimensions to minimise the excavation depth following the requirement that it be fully buried.

Plans and Contract Documents are being finalised.

3.5	Karori South Zone

This project will create the new larger zone and allow the decommissioning of the Allington Road Pumping Station and removal of the associated precast concrete tanks following the commissioning of the Karori South Reservoir.  A new main will be laid to connect the two parts of the zone.  The plans and Contract Documents have been prepared and tenders invited.

3.6	Eastern Suburbs Storage

There is a storage deficit in the Low Level Zone of 10 ML.  This was identified and reported on at the time of approval of the Macalister Park 20 ML Reservoir.  Of this storage, approximately 7 ML is required in the Eastern Suburbs (Miramar) and 3 ML in the Southern Suburbs (Island Bay).

Because these reservoirs will balance on the Low Level Zone, a very careful analysis is required to establish the optimum reservoir levels.  Additional pressure monitoring points have been established at the Moa Point Sewage Treatment Plant and Kilbirnie Crescent.  Network modelling was undertaken to establish levels for the reservoir at different sites, as well as enhancement required to the pipe network.

A preliminary analysis of the three potential sites has been made, which has indicated that one site has significant advantages.  A report has been prepared.

3.7	Work Related to the Facilities Management Contract

The maintenance of the Wellington City Council plan record system continues but advice has been received that this service will not be required after 30 June 2000.

Subdivisions are assessed for compliance with the Code of Practice for Land Development and approval given.

Project Information Memoranda (PIMs) and Land Information Memoranda (LIMs) are processed on a regular basis for the City Council.

4.	Other Projects

4.1	Rallywood Bridge

This bridge project for the Plantation Forestry Department has been investigated, designed and tenders invited.  A tender recommendation was made but the Contract will not be awarded until various agreements have been completed.  Arrangements have been made to extend the tender validity period.

4.2	Waterloo Car Parks

Construction work is almost complete on a project to fit in some more parking spaces at the Waterloo Bus/Rail Interchange.

4.3	Wellington City Bus Priority Lanes

This project is to arrange the implementation of bus priority lanes in four areas.  Progress has not been as rapid as hoped, largely because of the difficulty in obtaining appropriate information.

Laboratory Services

March/April 2000

Laboratory Services Department

Review of Operations for the Period Ended 30 April 2000

1.	Items of Note

- Summer sampling ended on 31 March 2000.

- Giardia and Cryptosporidium in small numbers were again detected at Wainuiomata River intake.  The numbers are low and appear to be consistent with the trend for this area.

2.	Financial

The operating surplus is below budget at this stage.  Although operating expenditure is slightly under budget currently, the reduced level of internal revenue significantly outweighs any direct cost savings.

3.	Business Summary

3.1	Quality

There were no requests for retesting samples and test reports are being sent out within the agreed time frames.

3.2	Health and Safety

There are no incidents to report.

Plantation Forestry

March/April 2000

Plantation Forestry Department

Review of Operations for the Period Ended 30 April 2000

1.	Log Harvest Contract

Another excellent month in March, with a total of 5,987 tonnes for a net revenue of $173,616.  April produced 3,198 tonnes for a net revenue of approximately $96,000.

March and April grade outputs have been:

|  | March | April |
| --- | --- | --- |
| Grade | Tonnes | % | Tonnes | % |
| Pruned domestic | 154 | 2.57 | 42.61 | 1.33 |
| Pruned export | 0 | 0 | 0 | 0 |
| Partial pruned | 0 | 0 | 0 | 0 |
| S Grade | 846 | 14.13 | 787.79 | 24.60 |
| A Grade | 619 | 10.34 | 111.92 | 3.50 |
| L Grade | 492 | 8.22 | 193.32 | 6.04 |
| R Grade | 0 | 0 | 0 | 0 |
| K Sawlog | 1,540 | 25.72 | 772.97 | 24.18 |
| K Rough | 338 | 5.64 | 316.75 | 9.91 |
| Pulp | 1,807 | 30.17 | 916.54 | 28.67 |
| O/S Pulp | 192 | 3.21 | 55.05 | 1.72 |

Domestic prices have increased following a marked increase in demand.  Increases of around $8 have been achieved for the better sawlog grades and more modest increases for pulp have resulted in a positive return from all but the most difficult stands.  Fletchers have been in the market for pulp to complete a shipment ex-Wellington.  Although there is little to choose from between them and our usual Wairarapa customer, the competitive factor will ensure neither of the parties become too complacent.

Export prices all moved down a few cents in response to changing exchange rates.

A cable hauler due in the forest by mid/late April finally arrived in the first week of May.  This should ensure the loggers are able to continue to work through the winter.

2.	Silviculture Contracts

Two hundred and twenty-five hectares of a total 306 hectares of the current year’s contract had been completed by 31 March, with the total at 235 as at 30 April.

The contractor having difficulty completing their block has not resumed work so they are to be officially advised that we consider their contract to be abandoned and we will award the balance of the work to another contractor.

3.	Plantation Forestry Operations

Although there was less rain in March, the lower temperatures have prevented the new trees from drying out and good growth has continued.  Even April with lower temperatures had low wind run and good growth resulted.

The results of the foliage analysis carried out in February are now to hand and planning is underway to fertilise 120 ha this autumn.

Some canker has shown up in the macrocarpa stands in Puketiro. There is no “cure” for this condition but we have undertaken additional thinning to improve the airflow through the block to minimise the risk.

4.	Forest Access

Maungakotukutuku is still isolated but this is not serious as no work is programmed in the near future.

The newly constructed roads into Pakuratahi East are holding up well.  A maintenance programme to be completed prior to winter has been agreed with the contractor and we are confident that harvesting will be possible through the winter months.

The Rallywoods agreement is still unsigned as various legal requirements remain to be settled.  While there is a will to complete the agreement, there is now a very real possibility that construction of the bridge will not be completed before the resource consent conditions require a cessation of work in the river on 1 June.

The design of the concrete battery ford for Puketiro continues and investigations are underway to find a suitable route for a logging road from Puketiro Road into the two MOT blocks.  It is planned to have the investigation completed in time for construction to commence next summer.

5.	Market Trends

Exports markets remained flat entering the new quarter but good increases were achieved in the domestic market.  We have now reached the point where most of the pulp from Pakuratahi makes a positive contribution to our bottom line.  This is a first in my time.

Cutting is to commence mid-May for the new mill at Waingawa and it is predicted that the type of tree at Pakuratahi will be ideal.  This is because of the restriction on the large end diameter that the plant can accept.

6.	Visitors

Approximately six months ago I received a request from the Wairarapa Branch of  Forest and Bird that they be allowed access to the Pakuratahi East Forest for a day trip.

This trip took place on 30 April and was very successful, with 39 members from both the Wairarapa and Wellington branches attending.  Most seemed supportive of Council’s policy regarding its commercial forestry activities and were grateful for the opportunity to visit the site while it was being logged.

7.	Reporting of Proposed Forestry Activities

Although the proposed activities of the Plantation Forestry Department are subject to Council scrutiny through the annual planning process, the detailed outcomes of the previous year’s results are not reported.  To overcome this situation it is suggested that in October of each year a paper be put before this Committee that sets out the results of the year completed to the previous 30 June and the proposals for the year to commence 1 July next, which will be fed into the annual planning process. This will allow Councillors the chance to consider the proposals before they form part of the proposed Annual Plan.

# Text boxes

Error! Not a valid link.

Error! Not a valid link.