Water Supply

May 2000

Operations Group

May 2000

Operations Group

Review of Operations for the Period Ended 31 May 2000

### 1.	Items of Note

- Periods of heavy rain have resulted in minor problems at the treatment plants because of high river colour and turbidity.

- The final commissioning of the system optimiser has been delayed until the beginning of June.  Initial impressions are that it will be extremely beneficial to the operation of the treatment plants.

2.	Water Quality

A total of 273 samples from trunk mains were tested for coliform organisms.  None of these samples tested positive.

Secchi disc water clarity in the Te Marua north lake varied between 4.7 m and 7.8 m, and in the south lake between 5 m and 8 m.  These are considered satisfactory.

The dominant phytoplankton were as follows:

- North Lake:  Oscillatoria, Synedra, Chlorella

- South Lake:  Synedra, Staurastrum, and Cosmarium.

Oscillatoria is a filter clogging algae when present in high concentrations.

Synedra produces a musty smell and slick tongue sensation when abundant

Staurastrum produces a grassy smell when abundant.

Dissolved oxygen and pH readings are also satisfactory.

Giardia and Cryptosporidium results were as follows:

Te Marua

Lakes		)	No Giardia

)	No Cryptosporidium

Intake		)	No Giardia

)	No Cryptosporidium

Treated Water	)	No Giardia

)	No Cryptosporidium

Wainuiomata

Treated Water	)	No Giardia

)	No Cryptosporidium

Lower George Creek	)	No Giardia

)	Low Cryptosporidium

Big Huia Intake	)	Low Giardia

)	No Cryptosporidium

Intake		)	Low Giardia

)	Low Cryptosporidium

George Creek South arm	)	Low Giardia

)	Low Cryptosporidium

Orongorongo

Intake 		)	Low Giardia

)	Low Cryptosporidium

During May 2000 17 transgressions were notified:

- 6 low fluoride

- 6 chlorine

- 4 presumptive coliform

- 1 high turbidity

3.	Supply Situation

The two monthly seasonal forecast for June and July 2000 issued by the Meteorological Service is as follows:

Situation as at June 10

For Wellington:

Rain:	Normal to slightly above normal

Wind:	More southerly winds than normal

Temperature:	Near normal

Sunshine:	About average

Specials:	Wet days from passing low pressure systems

Confidence:	Moderate

Local sea surface temperatures have been acting as a background heater and fooled some plants into a brief “false spring”.  However, as we move into winter, episodes of southerly winds are expected to become a recurring theme of the season.  Keep an eye on the weather map for low pressure systems deepening or lingering near Chatham Islands, for these can produce several days of chilling southerlies.

Hutt River Flows

The mean monthly river flow for the month of April was above average

Wainuiomata River Flows

Flow in the Wainuiomata River during April was average.

Aquifer Levels

The Waiwhetu aquifer level for April was above average.

4.	Production

4.1	Wainuiomata

4.1.1	Safety

There are no accidents or incidents to report.

4.1.2	Operations

- During the recent storm lightning damaged outlet magflow.  This has now been repaired.

- The new Wainuiomata intake flow meter has been installed but is not yet commissioned.

- Poor river conditions because of heavy rain have meant that the plant has been off on numerous occasions.

4.2	Waterloo Water Treatment Plant

4.2.1	Safety

There are no accidents or incidents to report.

4.2.2	Operations

- The optimiser project is changing the way all the plants behave.

- Reservoir B has been cleaned out as part of its routine maintenance.

- A lightning strike affected one variable speed well pump telemetry unit.

4.3	Gear Island

4.3.1	Safety

There are no accidents or incidents to report.

4.3.2	General

- The mechanical seal and motor was replaced on chlorine boost pump 1.

4.4	Te Marua

4.4.1	Quality

- Problems with the treatment process resulted in high aluminium levels in the treated water.   The plant outlet flow was diverted to Lake 1 until all filters had been backwashed and the treatment process reestablished.  This process problem is associated with treating lake water using direct filtration.  Until this problem is resolved lake water will be treated using the clarifiers.

- Fluoride dosing was shut down for the annual calibration of the weighing system.

- Low fluoride caused by plant staff failing to reset the system following a slam-shut the previous day.

4.4.2	Safety

There are no health and safety issues to report.

4.4.3	Operations

15 May:		A slam-shut was caused by a poor cable connection in the chlorine local control panel.

21 May:		Supernatant lagoon high level alarm caused by strong wind and wave action.

28 May:		Plant slam-shut caused by grit particles in the treated water turbidimeter.  The sample cell was rinsed out and the instrument returned to service.

30 May:		Pumping station treatment pumps began operating erratically.  The problem was traced to faulty telemetry equipment requiring software modifications.

31 May:		The plant was shut down for the day to allow a new magnetic flow meter to be installed in the main outlet pipeline.

Ongoing problems with Filter No. 1 penstock have now been resolved.  The intermittent fault was caused by a faulty proximity sensor, which has been replaced.

4.4.4	Plant Tours

2 May:			Wellington Regional Council induction : 15 people

29 May:		Central Institute of Technology NZCE students : 11 people

4.4.5	General

- The installation of lake telemetry and instrumentation to improve lake monitoring and alarms is well underway and due for complete in late June.

5.	Distribution

5.1	Electrical/Pipeline Sections

5.1.1	Flow Meters

- New electromagnetic flow meters have been installed for:

- Thorndon

- Maldive No. 1 Reservoir inlet

- Maldive No. 2 Reservoir inlet

- Kelburn Reservoir inlet

- Wainuiomata outlet

- Naenae : at Waterloo Water Treatment Plant

- Wainuiomata inlet

- Te Marua outlet

These meters have been connected to the telemetry system.

- Problems occurred during the installation of the electromagnetic flow meter on the Waterloo outlet to Naenae.  The prepared action plan failed to identify a “dead leg” of pipework, which was inadvertently brought into operation as a result of the valve operations necessary to isolate the section of pipe in which the electromagnetic flow meter was to be installed.  A dead leg is a section of pipe through which water does not normally flow or a section of pipe that is normally valved off containing water.  The operation of this section of pipe resulted in high turbidity water being distribution into the Hutt Central Business District.  This resulted in complaints being received by Hutt City Council from domestic and business customers.  We have no indication of the magnitude of the complaints received but have notified our insurers of the potential liability.

In order to reduce the possibility of a similar incident recurring we have reviewed the pipe reticulation and identified potential dead legs.  We have also included a heading in our draft action plans referring specifically to “dead legs”.  This will act as a prompt for people responsible for preparing these action plans, which are necessary when carrying out any work that interacts with our distribution treatment or reticulation system.

During the incident we liased with Hutt City Council staff in order to establish a flushing routine and our staff took samples from affected properties.  No problems were identified with the analysis of samples taken.

5.1.2	Haywards Optimisation

- Work has started on stage 1, excavation for the new inlet main and new valve chamber to No. 2 Reservoir, and removal of anchor blocks, redundant pipework and valves.

5.1.3	Buick Street Decommissioning

- The 375 mm water main connection Buick Street Pumping Station to the reticulation has been blanked off.

- All useful electrical instrumentation and equipment have been removed.

5.1.4	Karori Decommissioning

- Ongoing work with the contractors on the Kelburn branch line has been carried out.

5.1.5	1050 mm Pipeline

- Pipeline maintenance has proceeded on the 1050 mm pipeline between the Ngauranga valve chamber and Thorndon Pumping Station.

6.	Health and Safety : Total Injury/Illness/Incident Record

Production

There are no accidents or incidents to report.

Distribution

There are no accidents or incidents to report.

Network

There are no accidents or incidents to report.

Operations Network

Review of Operations for the Period Ended 31 May 2000

### 1.	Items of Note

- During the period five burst mains were reported and all repaired within the allotted time frame.

### 2.	Water Supply (PT 30.1)

3.	Financial

### Facilities Management Contract

Contract Amounts : Wellington, Including Tawa

| Month | Actual $ | Budget $ | Variance % | Year to Date | Budget $ | Variance % |
| --- | --- | --- | --- | --- | --- | --- |
| May | 223,343 | 294,314 | -24.11% | 2,502,159 | 3,237.454 | -22.71% |

### 4.	Water Quality

### 4.1	Routine Testing (PT 1.1)

The water quality was monitored and the appropriate laboratory tests were completed for May.  There were 136 samples from the reticulation system tested for bacteriological compliance.  Compliance for the month is 100 percent.  Compliance for the year to date is 100 percent.

### 4.2	Water Tests Initiated by Customers (PT 2)

|  |  | May | Year to Date | Compliance Year to Date (%) |
| --- | --- | --- | --- | --- |
|  | Number received | 7 | 93 | - |
| (PT 2.2) | Within ability of Operations Network to control | 2 | 18 | - |
| (PT 2.1) | Formal response within five days | 7 | 89 | 96% |

### 5.	Customer Services

### 5.1	Counter and Other Office Services (PTs 3.1, 4.1, 5.1)

Information has been provided to customers requesting information by letter, telephone and over the public counter.  A breakdown of enquiries received during the reporting period is as follows:

|  | May |
| --- | --- |
|  | Counter enquiries | 95 + 15 encroachments |
|  | Proposals from other utilities | 9 |
| (PT 33.1) | Plan records : New services recorded | 22 |
|  | Response time requirement compliance | 100% |

### 5.2	Complaints Register (Monthly Summary) (PT 5.1)

An enquiry/complaints register is being maintained.

A breakdown of complaints and enquiries received during the reporting period is as follows:

|  | May |
| --- | --- |
| (PT 2.2) | Water quality | 7 |
| (PT 16.1.2) | Pressure | 11 |
| (PT 20.1) | Reinstatement | 0 |
| (PT 16.1.4) | No-water | 26 |
|  | Contractors | 0 |
|  | Other | 0 |

All of the Water Quality, Pressure and No-water complaints were responded to and completed within the performance criteria.

### 6.	Response Maintenance

### 6.1	Compliance (PTs 9.1, 9.1a, 9.2, 10.1, 16.1)

|  | May |
| --- | --- |
|  |  | No. of Calls | Completed to Standard | Compliance % |
| (PT 9.1) | Stopcocks | 399 | 347 | 86 |
| (PT 9.1) | Hydrants | 94 | 85 | 90 |
| (PT 9.1a) | Valves | 27 | 22 | 81 |
| (PT 9.2) | Other leaks | 202 | 176 | 87 |
| (PT 10.1) | Mark-outs | 52 | 52 | 100 |
| (PT9.1a) | Value repacks | 12 | 12 | 100 |
| (PT 16.1.1) | Burst mains | 5 | 5 | 100 |
| (PT 2.1) | Water quality complaints | 7 | 7 | 100 |
|  |  | 798 | 706 | 88 |

Failures

|  | May |
| --- | --- |
|  | Jobs Failed by 1-24 Hours | Jobs Failed by1-5 Working Days | Jobs Failed >5 Working Days |
| Fire hydrants | 2 | 2 | 5 |
| Mains | 1 | 1 | 0 |
| Valve repacks | 0 | 0 | 0 |
| Valves | 0 | 3 | 2 |
| Services | 13 | 8 | 3 |
| Tobies | 14 | 29 | 9 |
| Total | 30 | 43 | 19 |

Additional Work Carried Out

|  | May |
| --- | --- |
| New services | 22 |
| Damages by contractors | 31 |
| Variations | 8 |
| Renewals over 4 m | 6 |

### 6.2	Burst Mains (PT 16.1)

There were five burst mains during the month of May, these being as follows:

Cnr Black Rock and Newlands Roads	2 May 2000

Station Road (50 m from railway station)	7 May 2000

35 Rothsay Road	7 May 2000

36-54 Kingsford Smith Street	28 May 2000

Cnr Ariki Road and Hepara Street	30 May 2000

All burst mains were attended to within 30 minutes and repaired within 8 hours.

### 6.3	Supply (PT 16.1)

|  | May |
| --- | --- |
| Total calls regarding loss or temporary loss of supply because of broken mains or supply failure | 26 |
| Total calls attended within 30 minutes | 26 |
| Total Compliance | 100% |

### 6.4	Reinstatement (PT 20.1)

There were no complaints received this month regarding trench reinstatements.  The Facilities Management Contract target is less than 12.

### 6.5	Shutdown Notification (PT 6.1)

There were 18 planned shutdowns during May.  All identifiable customers received notification within 24 hours prior to the shutdown.

### 6.6	Locates and Investigations (PT 10.1)

Work completed during the period comprised:

|  | May |
| --- | --- |
| Locate stopcocks | 100 |
| Leak location | 160 |
| Flow tests | 0 |
| Seepage/Investigations | 8 |
| Miscellaneous supply jobs | 9 |

### 7.	Health and Safety

There were no incidents reported this month.

### 8.	Meters (PT 13.1)

A total of 1,492 suburb and high use meters were read, and entered into the system by 23 May 2000.

9.	Pumping Stations, Reservoirs and System Control

### 9.1	General

Normal routine maintenance has resulted in the Wellington City system operating satisfactorily.

### 9.2	Control System (PT 30.1)

The control system continues to operate satisfactorily.  The radio in the Hay Street telemetry unit was replaced because of frequent communication failures.

### 9.3	Birch Street Pressure Control Valve

The pressure control valve at Birch Street was overhauled.

### 9.4	Thorndon Pumping Station

One of the two pressure reducing valves at Thorndon Pumping Station has been dismantled.  Replacement parts from the United States are awaited so that the pressure reducing valve can be rebuilt.

### 9.5	New Flow Meters

No new electromagnetic flow meters were installed during the month.

### 9.6	Maintenance Checks (PT 17.4)

Maintenance has been carried out as follows:

| May |
| --- |
| Round A | Round B |
| Rajkot Terrace Nassau Avenue Mark Avenue Chapman Street Burnside Road Ruskin Road Broderick Road Broadmeadows High Pump Station Satara Street Kitchener Terrace Davies Road CV Birch Street CV Ohariu CV Glover Street CV Ironside CV | Huntington Street Warwick Street Hay Street Epuni Street Mapuia Street/Mt Crawford Sar Street Alexander Road Redwood Greyfriars Road Bell Road CV Webb Street CV Prince of Wales CV Vasanta CV |

### 10.	Development

### 10.1	Development Statistics

| Subdivisions | May | Year to Date |
| --- | --- | --- |
| Construction plans approved (lots/units) | 8 | 236 |
| Scheme plans approved | 39 | 343 |
| Subdivisions cleared (lots/units) | 107 | 600 |

### 10.2	Development Projects

10.2.1	Churton North Reservoir

The reservoir was filled for the first time and allowed to stand for seven days to check for leaks.  There was no measurable fall in water level but there were a few minor visible leaks that are being repaired.

The consultants have stated that they will use mains power rather than solar/batteries.

Chlorination is expected to start on 19 June and commissioning within two weeks after that.

10.2.2	Westchester Drive Pumping Station and Rising Main

Extra bracing struts have been installed and the eccentric tapers turned over.  The noise test showed that the noise levels were within required District Plan levels.

10.2.3	Subdivisional Financial Contributions

Various letters and reports on current and proposed contributions were sent to Wellington City Council for consideration and approval.

10.2.4	Major Subdivisions

Construction plans were submitted for approval of the following major subdivisions:

- Lots 25 and 26, Waverton Terrace, Churton North (2 lots).  This has not yet been finally approved, as plan amendments have been requested.

- Lot 5, Glanmire Road, Newlands (1 lot).  This has not yet been finally approved, as plan amendments have been requested.

- Rossaveel Heights, Stage 3, Tawa (19 lots).  This has not yet been approved, as we have requested amended plans from the developer.

- de Bes Subdivision, Beacon Hill (5 lots).  Amended plans were received on 29 May and are currently under consideration.

- 15 Glanmire Road, Newlands (6 lots).  Approved 19 May 2000.

- 138 Queens Drive, Lyall Bay (6 lots).  This has not yet been finally approved, as plan amendments have been requested.

- Greenvue, Stage 10, Tawa (8 lots).  Plans were received on 24 May and are currently under consideration.

- Greenvue, Stage 10B, Tawa (3 lots).  Plans were received on 29 May and are currently under consideration.

As-built plans were submitted for approval for the following major subdivisions:

- Kim Street/Burma Road (5 lots).  This has not yet been cleared, as completion of outstanding work is awaited.

- Bellevue, Stage 6, Newlands (27 lots).  Cleared 18 May.

- Tattenhall Grove and Hetsby Place, Churton North.  The plan was received on 29 May and is currently under consideration.

10.2.5	Fire Services Recently Connected (PT 12.1)

There were no fire services connected during the month.

10.2.6	New Commercial Metered Services

There was one new commercial metered services connected during the month:

- 2 Torrens Terrace, Te Aro : 20 mm (25 May)

### 10.3	Building Development Appraisals

|  | May |
| --- | --- |
|  | Commercial | Domestic |
| Building consents | 7 | 48 |
| PIMS applications | 9 | 52 |
| Compliance with response time requirement | 100% | 100% |

10.4	Land Information Memorandum

|  | May |
| --- | --- |
| Applications processed | 48 |
| Compliance with response time requirement | 100% |

### 11.	Capital Works

### 11.1	Main Laying : City

### 11.1.1	Contracts in Maintenance Period

The following pipelaying contracts in the central city are in the maintenance period:

- Manners Street

- Cuba Street

### 11.1.2	Taranaki Street

Contract Documents are about to be submitted to Wellington City Council for the replacement of the 150 mm cast iron and 150 mm asbestos cement mains in Taranaki Street.

### 11.2	Main Laying : Suburbs

### 11.2.1	Contracts in Maintenance Period

The following pipelaying contracts are in the maintenance period:

- Makara Road Rising Main

- Owhiro Bay Parade

- Helston Road

- Rider Main Renewals

- Fox Street

The maintenance period for the Tirangi Road, Kingsford Smith Street and George Bolt Street Contract has expired.  The Contractor has been asked to rectify some minor issues before the maintenance retentions are released.

The maintenance periods for the Bracken Road and Breaker Bay Road Contracts have expired and the maintenance retentions have been released.

### 11.2.2	Bell Road Zone Improvements

The Contractor is undertaking the final connections and reinstatement to complete the works.

### 11.3	High Level Distribution and Storage

### 11.3.1	Karori South and Allington Road Zones Amalgamation

Works Infrastructure Ltd was awarded the Contract to install a pipeline to link the Karori South and Allington Road water supply zones.

Work has just started on-site.

### 11.3.2	Wadestown Reservoir

The consultant has virtually completed the Contract Documents.  The pipework and electrical drawings and specifications have been completed.  The condition of the existing pipeline to be used as a scour/overflow for the reservoir is being investigated.  Wellington City Council is considering how to arrange the bonds required by the resource consent.

### 11.3.3	Grenada North High Level Reservoir

The consultant is addressing the issues raised about the draft Contract Documents.  Additional information has been provided in response to queries raised during the resource consent application process.

### 11.4	Low Level Zone Storage

11.4.1	Eastern Suburbs Reservoir

The report on the preliminary assessment of the potential reservoir sites has been prepared and distributed.

| Analysis - December 1998 to May 2000 |
| --- |
|  | Quality Reports PT 2.1 | No of Planned Shut-downs PT 6.1 | Stopcocks PT 9.1 | Leaking Hydrants PT 9.1 | Leaking Valves PT 9.1a | Leaks PT 9.2 | Mark-outs PT 10.1 |
|  | Calls Received | 5 Day Response | % Compl. | Completed | Calls Received | Completed | % Compl. |  | % Compl. |  | % Compl. | Calls Received | Completed | % Compl. | Received | % Compl. |
| July 1998 | 8 | 8/8 | 100% | 2 | 371 | 359 | 96% | 90 | 94% | 24 | 100% | 231 | 213 | 95% | 61 | 95% |
| August 1998 | 10 | 17/18 | 94% | 2 | 304 | 243 | 87% | 91 | 86% | 25 | 100% | 216 | 183 | 85% | 74 | 100% |
| September 1998 | 11 | 26/29 | 90% | 4 | 289 | 211 | 81% | 71 | 77% | 13 | 100% | 219 | 183 | 84% | 74 | 100% |
| October 1998 | 6 | 32/35 | 91% | 3 | 385 | 293 | 73% | 107 | 73% | 6 | 100% | 216 | 147 | 68% | 67 | 100% |
| November 1998 | 7 | 37/42 | 88% | 3 | 421 | 382 | 76% | 70 | 75% | 13 | 100% | 228 | 198 | 86% | 91 | 100% |
| December 1998 | 9 | 46/51 | 92% | 2 | 365 | 362 | 90% | 79 | 78% | 9 | 100% | 234 | 233 | 99% | 16 | 100% |
| January 1999 | 13 | 59/64 | 93% | 25 | 431 | 429 | 99% | 77 | 64% | 15 | 93% | 275 | 271 | 98% | 21 | 100% |
| February 1999 | 10 | 69/74 | 93% | 30 | 343 | 336 | 97% | 106 | 81% | 18 | 94% | 176 | 170 | 96% | 11 | 100% |
| March 1999 | 5 | 74/79 | 94% | 34 | 488 | 359 | 74% | 118 | 94% | 12 | 92% | 324 | 282 | 84% | 108 | 100% |
| April 1999 | 5 | 79/84 | 94% | 18 | 430 | 367 | 85% | 129 | 91% | 20 | 95% | 259 | 221 | 85% | 94 | 100% |
| May 1999 | 8 | 86/92 | 93% | 18 | 366 | 285 | 78% | 110 | 78% | 10 | 80% | 239 | 200 | 84% | 140 | 100% |
| June 1999 | 5 | 90/97 | 93% | 18 | 364 | 269 | 74% | 90 | 68% | 21 | 95% | 262 | 204 | 77% | 86 | 100% |
| Summary (1998/9) | 97 | 90/97 | 93% | 159 | 4557 | 3915 | 86% | 1138 | 81% | 186 | 96% | 2879 | 2505 | 87% | 823 | 99% |
| July 1999 | 16 | 15/16 | 94% | 18 | 385 | 345 | 92% | 72/78 | 92% | 18/19 | 95% | 267 | 258 | 96% | 47 | 100% |
| August 1999 | 6 | 6/6 | 100% | 15 | 347 | 333 | 91% | 85/89 | 96% | 16/19 | 84% | 241 | 225 | 98% | 51 | 100% |
| September 1999 | 1 | 1/1 | 100% | 12 | 356 | 275 | 82% | 68/72 | 94% | 18/20 | 90% | 276 | 226 | 82% | 41 | 100% |
| October 1999 | 13 | 13/13 | 100% | 21 | 320 | 241 | 75% | 71/87 | 81% | 19/20 | 95% | 234 | 198 | 85% | 40 | 100% |
| November 1999 | 12 | 12/12 | 100% | 16 | 365 | 334 | 92% | 81/92 | 88% | 11/13 | 85% | 246 | 228 | 93% | 30 | 100% |
| December 1999 | 4 | 4/4 | 100% | 8 | 364 | 346 | 95% | 77/80 | 96% | 21/32 | 66% | 218 | 194 | 89% | 28 | 100% |
| January 2000 | 3 | 3/3 | 100% | 0 | 391 | 341 | 87% | 77/94 | 82% | 18/26 | 69% | 237 | 182 | 77% | 40 | 100% |
| February 2000 | 9 | 7/9 | 78% | 6 | 467 | 389 | 83% | 102/117 | 87% | 19/25 | 76% | 222 | 196 | 88% | 57 | 100% |
| March 2000 | 15 | 14/15 | 93% | 46 | 473 | 405 | 86% | 105/134 | 78% | 14/17 | 82% | 247 | 204 | 83 | 24 | 100% |
| April 2000 | 7 | 7/7 | 100% | 17 | 312 | 278 | 89% | 100/114 | 88% | 13/27 | 48% | 181 | 152 | 84% | 28 | 100% |
| May 2000 | 7 | 7/7 | 100% | 18 | 399 | 347 | 86% | 85/94 | 90% | 22/27 | 81% | 202 | 176 | 87% | 52 | 100% |
| Running Total for Current Year | 93 | 89/93 | 96% | 177 | 4,179 | 3,634 | 87% | 923/1070 | 86% | 189/245 | 77% | 2,571 | 2,239 | 87% | 438 | 100% |
| Analysis - December 1998 to May 2000 |
|  | Loss of Supply PT 16.1 | Burst Mains PT 16.11 | Reinstatements PT 20.1 | Toby Locates | Damage Repairs | Total Calls |
|  | Complaints Received | % Compl. | Occurred | % Compl. | Occurred | % Compl. |  |  | Calls Received | Completed | % Compl. |
| July 1998 | 29 | 97% | 6 | 100% | 3 | 100% | 81 | 91 | 791 | 753 | 95% |
| August 1998 | 31 | 97% | 2 | 100% | 4 | 100% | 89 | 100 | 703 | 613 | 81% |
| September 1998 | 30 | 100% | 8 | 100% | 1 | 100% | 97 | 98 | 683 | 553 | 81% |
| October 1998 | 29 | 83% | 5 | 100% | 0 | 100% | 72 | 57 | 795 | 605 | 76% |
| November 1998 | 24 | 96% | 9 | 90% | 3 | 100% | 89 | 103 | 838 | 751 | 90% |
| December 1998 | 15 | 80% | 4 | 100% | 1 | 100% | 101 | 26 | 770 | 763 | 99% |
| January 1999 | 21 | 100% | 7 | 100% | 1 | 100% | 92 | 23 | 875 | 868 | 99% |
| February 1999 | 25 | 96% | 5 | 100% | 0 | 100% | 100 | 29 | 647 | 630 | 97% |
| March 1999 | 32 | 97% | 8 | 100% | 0 | 100% | 102 | 102 | 1073 | 884 | 82% |
| April 1999 | 46 | 94% | 7 | 100% | 1 | 100% | 64 | 46 | 945 | 831 | 88% |
| May 1999 | 32 | 100% | 2 | 100% | 1 | 100% | 81 | 109 | 875 | 729 | 83% |
| June 1999 | 33 | 85% | 7 | 100% | 3 | 100% | 80 | 105 | 837 | 655 | 78% |
| Summary (1998/9) | 347 | 94% | 70 | 99% | 18 | 100% | 1048 | 889 | 9832 | 8635 | 88% |
| July1999 | 19/22 | 86% | 8 | 100% | 4 | 100% | 91 | 75 | 830 | 767 | 92% |
| August 1999 | 14/16 | 88% | 9 | 100% | 0 | 100% | 85 | 34 | 807 | 735 | 91% |
| September 1999 | 50/50 | 100% | 9 | 100% | 1 | 100% | 75 | 54 | 777 | 640 | 82% |
| October 1999 | 17/17 | 100% | 4 | 75% | 0 | 100% | 76 | 22 | 724 | 591 | 82% |
| November 1999 | 9/10 | 90% | 8 | 100% | 1 | 100% | 72 | 29 | 774 | 709 | 92% |
| December 1999 | 23/23 | 100% | 5 | 100% | 1 | 100% | 64 | 20 | 744 | 681 | 92% |
| January 2000 | 3/4 | 75% | 7 | 100% | 0 | 100% | 83 | 16 | 809 | 677 | 84% |
| February 2000 | 2/2 | 100% | 5 | 100% | 0 | 100% | 135 | 58 | 909 | 783 | 87% |
| March 2000 | 8/8 | 100% | 4 | 100% | 0 | 100% | 113 | 41 | 929 | 782 | 84% |
| April 2000 | 8/9 | 89% | 5 | 100% | 3 | 100% | 73 | 18 | 701 | 600 | 86% |
| May 2000 | 26/26 | 100% | 5 | 100% | 0 | 100% | 100 | 31 | 798 | 706 | 88% |
| Running Total for Current Year | 179/187 | 96% | 69 | 98% | 10 | 100% | 967 | 398 | 8,802 | 7,671 | 87% |

Strategy and Asset Group

May 2000

Strategy and Asset Group

Review of Operations for the Period Ended 31 May 2000

### 1.	Items of Note

- The benchmarking process for 1998/99 has been reviewed with Watercare Services.  Most of the participants in the survey provide water from source to tap.  It is proposed to simplify the survey for Watercare and the Wellington Regional Council so it is more applicable to our wholesale functions.

- A presentation will be made to the Committee of the 1998/99 benchmarking results.

- An agreement with Hutt City Council for the provision of a non-fluoridated water supply to the Rahui Reservoir is being finalised.  See a separate Committee report.

- A customer meeting was held to explain the 2000/01 Capital Works Programme.

- Loading the asset values into the asset management database and reconciling them has been a major exercise.

### 2.	Sales Volume : Water Consumed from 1 April to 31 May 2000

- There is a marginal difference in consumption over the same period last year.  Subject to Council approval, there will be a 4 percent reduction in the levy.

3.	Asset Management

- The book value of the Infrastructure Assets has been finalised at $251,303,074.  Discussions are continuing with Finance Division on the transition from the old fixed asset register to the Hansen system, year end capitalisation procedures and monthly calculation of depreciation.

- A review of the June 1998 Asset Management Plan has been commenced, but no significant changes will be made until 2001.

- Capital works for 1999/2000 are close to completion.  The projected full year expenditure on capital works for 1999/2000 is $3.627 million, against a budget of $4.165 million.  An amount of $400,000 will be rebudgeted to 2000/2001 to complete projects that have been delayed.

- Commissioning of stage 1 of the System Optimiser is targeted for completion early in June.  The System Optimiser will select water sources and manage pump use to minimise the cost of the production and distribution of water.

- The Buick Street Pumping Station has been demolished and the wells sealed.  Design work on a system to supply unfluoridated water to Petone from Waterloo has begun.

- Decommissioning work at Karori Reservoir is close to completion.  A very large steel pressure vessel has recently been sold and removed from the site.  Minor tidy up and resealing remains to be done.

- A resource consent application for a new well tapping the Moera Aquifer at Gear Island is being prepared.  A new well may affect IBM’s firefighting wells.  To check this, tests on the IBM well have been arranged.  An investigation bore drilled into the Moera Aquifer near Ewen Bridge by the Resource Investigations Section is currently being tested.

- Applications and Environmental Assessments for new surface water take consents have been submitted to the Environment Division for their consideration.  The applications will be formally notified about mid-June.

- Detailed seismic review and risk assessment work has been carried out for a number of network elements, and some strengthening works are proposed for 2000/2001 as a result.  A detailed risk study of the risks associated with the Silverstream Bridge has been carried out by Upper Hutt City Council.  The implications of the analysis for the water main on the bridge are being evaluated.

- A Risk Policy, which will provide broad guidelines for the management of risks to the water business, has been prepared.  A separate report is included in the Order Paper.

- The Wainuiomata ranger reports a relatively quiet month, although a number of unauthorised groups and individuals were encountered in the catchment over the Easter holiday period.  An additional warning sign has been erected in the Orongorongo Valley at the southern extremity of Wellington Regional Council land to discourage entry by the public.

- The annual Te Marua Lakes Data Report has been compiled and the data reviewed by a specialist consultant. The data shows that the lake embankments continue to behave in a safe and predictable fashion.

4.	Quality Assurance

- Statistical analyses of turbidity readings to demonstrate compliance with the rule that requires turbidity to be less than 0.5 NTU for 95 percent of the time have been carried out.  The results for May are set out below.  The percentage of the time turbidity is less than 0.1 NTU has also been calculated.

| Percentage Compliance | Turbidity <0.5 NTU | Turbidity <0.1 NTU |
| --- | --- | --- |
| Plant | May | May |
| Te Marua | 99.99% | 98.55% |
| Wainuiomata | 99.99% | 94.38% |

The >0.2 NTU change within 10 minutes rule has been tested for both plants.  This rule identifies “spikes” in the turbidity results, which have the potential to carry protozoa into the treated water.  The results are as follows:

| No. of Exceedances |
| --- |
| Plant | May |
| Te Marua | 0 |
| Wainuiomata | 12 |

These rules are intended to reduce the risk of Giardia and Cryptosporidium passing through the plant.  The plants incorporate “slam shut” valves so that any water that does not comply with the 0.5 NTU rule is not delivered to the customers.

- Work is continuing on the proposed Environmental Management System being developed under the provisions of ISO 14001.  An initial document audit was carried out by the international accreditation agency BVQI on 21 March.  The auditor raised a number of issues, and these are currently being addressed.  The final certification audit is scheduled for 19/20 June.

5.	Marketing

5.1	Market Research : Summer Water Conservation Campaign

- A PowerPoint presentation of results has been compiled and presented to Utility Services’ managers.  Customers will receive this presentation shortly.  A presentation will be made to the Utility Services Committee during the meeting.

5.2	Public Relations

- Provided details about sealing off the bore that connected Buick Street Pumping Station to the Hutt aquifer to the Hutt News.  An article, entitled Buick Street pump station runs dry after 37 years was published in the 16 May 2000 edition.

- Provided a draft media release to Wellington Regional Council Communications in response to a published release from the Health Research Council that implied that high levels of gastrointestinal disease in Wellington were because of tap water.  Communications’ media release Tummy bugs not from tap water, says WRC was released on 2 June.  Further details are included in a water quality update report.

- Provided a draft media release to Wellington Regional Council Communications to coincide with Report 00.210, Public Perception of Water Quality being presented to the Utility Services Committee.

- Provided Wellington Regional Council Regional Parks with photographic material and narrative for display at the Te Marua Pumping Station, as part of the Arbour Day Millennium totara planting.

5.3	Other Activities

- A first draft of topics for inclusion in The Water Group’s Annual Report of Business Activity has been researched and presented to managers for comment.  Photographic content has also been considered.

- Agreement has been reached with Upper Hutt City Council so that the Wellington Regional Council Metropolitan Leak Detection Programme can be continued.  Upper Hutt City Council had indicated previously that it was reluctant to pay this part of the water levy.

- Planning continued for Utility Services’ involvement in the Upper Hutt Science Festival, a programme to promote the role of science in the community.  An open day at Te Marua involving presentations and a guided tour is being planned for Saturday, 22 July, in conjunction with Operations and Laboratory Services.

- Progression of work regarding Utility Services and Environment working together to ensure that Environment’s Learnwell programme being developed for water conservation will address Utility Services’ objectives for educational material, as well as Environments.

5.5	Economics

- The new wholesale water database has now been running for approximately eight months.  Minor teething problems have been fixed and an instruction manual compiled.  An automated reporting process is being advanced.

- A time dependent database package suitable for the storage of data from the telemetry system is currently being evaluated.

6.	Projects Undertaken by Engineering Consultancy for the Strategy and Asset Group

- Te Marua Lakes to Treatment Plant Pipelines

This Contract is in the maintenance period.

- Kaitoke Weir Repair

The Contract for repairing the Kaitoke Weir is in maintenance.  Additional minor repair work is proposed during the low river flow period next summer.

- Kaitoke Concrete Pipeline

Repair works to the joints on the concrete pipeline between the Kaitoke Flume Bridge and the No. 2 Tunnel entrance are proposed.  Details of suitable materials for this work are being obtained from the suppliers and a report is being prepared.

- Branch Line to Plateau Reservoir

Upper Hutt City Council has requested a direct connection from the Kaitoke main to the Plateau Reservoir at Te Marua.  The design and preparation of the Contract Documents are nearing completion.

- Silverstream Scour on Kaitoke Main

A drawing detailing a new connection and scour for the Kaitoke main at Silverstream has been prepared.  Further work on this is on hold until August 2000.

- OK Main Slip Lining : Waiapu Road to The Rigi

The Contract for slip lining the OK main between The Rigi and Waiapu Road is in maintenance.

- OK Main Cement Mortar Lining : Thorndon to Karori

The Contract Documents for the cement mortar lining of the OK main between Thorndon and Karori are nearing completion.

- OK Main Crossing of Korokoro Stream

The OK main between Randwick and Korokoro supplies water to the new Rahui Reservoir.  The pipe crossing the Korokoro Stream is corroded and poorly supported.  Design of the proposed replacement crossing is proceeding.

###### Plimmerton/Pukerua Bay Branch Pipeline Shut-off Valve

The valve chamber and shut-off valve have been installed.  The automatic control of the valve has been commissioned.  Some minor adjustments are proposed.

- Hutt Estuary Bridge Pipelines

An order has been placed for the supply of flexible couplings for our pipelines on the Hutt Estuary Bridge to accommodate the design movement of the bridge in a seismic event.

- Buick Street Pumping Station Decommissioning

The two wells have been plugged and the pumping station building demolished.  The site is being reinstated.   Arrangements are being made to disconnect the rising main in Jackson Street.

#### Karori Reservoir Rationalisation

All major pipework alterations are complete and the site has been cleaned up.  A recoil check valve has been installed on the Kelburn rising main.  Pressure transmitters have been installed on the pump suction and delivery of the Kelburn pumps.

- Haywards Reservoir Utilisation

New control valves and pipework are being installed at Haywards Reservoir.  This is to allow remote control, turnover in the reservoir to maintain water quality and greater utilisation of the available water storage.

- Water Meter Replacement Programme

All water meters in the 1999/2000 replacement programme have been installed.  Arrangements are being made to use the new meters for revenue and calculation purposes.

- Te Marua Lakes Surveillance Manual

The condition of the Te Marua Lakes’ embankments and structures is regularly monitored.  The monitoring procedures are detailed in the Te Marua Lakes Surveillance Manual.  This manual is being updated.  The draft revised manual has been circulated and comments received for incorporating in the final issue.  A draft emergency action plan is being prepared.

Engineering Consultancy Group

May 2000

Engineering Consultancy Group

Review of Operations for the Period Ended 31 May 2000

1.	Work Carried Out for the Strategy and Asset Group

The main capital projects for which the Engineering Consultancy Group has responsibility are itemised in the Strategy and Asset Group report.  Support is also provided for other projects being undertaken by this group.

2.	Work carried Out for the Operations Group

The Engineering Consultancy Group has continued to provide support for smaller projects arising from the operation and maintenance of the wholesale water supply system.

3.	Work carried Out for Wellington City Council

3.1	General

Current projects underway are detailed in the following sections.

3.2	Pipeline Projects

Work commenced and is nearing completion for main laying in Rolleston Street, Salisbury Avenue, Salisbury Terrace and adjustment to the Bell Road Zone.  This work will resolve a longstanding low pressure problem in this area.  In addition, the abandoned Bidwill Street pressure maintaining tank has been demolished.

Contract Documents are being prepared for a replacement main to be laid in Taranaki Street from Courtenay Place to Webb Street.  This will be difficult because of the extensive underground services, as well as the constraints arising from the route being on State Highway.

3.3	Grenada North High Level Reservoir

This permanent reservoir, 160 m³ capacity, will replace the Grenada North temporary tanks.  The site is at a higher level to the east of Nassau Avenue on land that has recently been transferred from TransPower to Wellington City Council.  The intention of this reservoir and associated pipework is the second stage in the upgrade of the Grenada North water supply following the contamination incident in early 1998.

The consultants have prepared draft plans and Contract Documents.  These are undergoing further review.

3.4	Wadestown Reservoir

Montgomery Watson Ltd was engaged for the design of a replacement reservoir, capacity 1,800 m³, along with the obtaining of resource consents necessary for the completion of the reservoir on the Town Belt, as well as for access across the Town Belt.

The plans and Contract Documents are almost complete.  These incorporate the pipework and electrical/controls sections prepared in this office.  There are some hold-ups arising from the various internal Wellington City Council approvals required.

3.5	Karori South Zone

This project will create the new larger zone and allow the decommissioning of the Allington Road Pumping Station and removal of the associated precast concrete tanks following the commissioning of the Karori South Reservoir.  A new main will be laid to connect the two parts of the zone.  A Contract was awarded and work is about to start.  The Contract includes the demolition of the redundant structures.

3.6	Eastern Suburbs Storage

There is a storage deficit in the Low Level Zone of 10 ML.  This was identified and reported on at the time of approval of the Macalister Park 20 ML Reservoir.  Of this storage, approximately 7 ML is required in the Eastern Suburbs (Miramar) and 3 ML in the Southern Suburbs (Island Bay).

Because these reservoirs will balance on the Low Level Zone, a very careful analysis is required to establish the optimum reservoir levels.  Additional pressure monitoring points have been established at the Moa Point Sewage Treatment Plant and Kilbirnie Crescent.  Network modelling was undertaken to establish levels for the reservoir at different sites, as well as enhancement required to the pipe network.

A preliminary analysis of the three potential sites has been made, which has indicated that one site has significant advantages.  A report has been prepared and submitted to Wellington City Council.  A response is still awaited.

3.7	Work Related to the Facilities Management Contract

The maintenance of the Wellington City Council plan record system continues.  The details of this service after 30 June 2000 will change because of the move away from paper records.  The exact new scope of work is still being resolved.

Subdivisions are assessed for compliance with the Code of Practice for Land Development and approval given.

Project Information Memoranda (PIMs) and Land Information Memoranda (LIMs) are processed on a regular basis for the City Council.

4.	Other Projects

4.1	Rallywood Bridge

The various agreements have now been entered into so the Contract was finally awarded to Works Infrastructure Ltd.  Work on-site is programmed to commence on 3 July 2000.

4.2	Wellington City Bus Priority Lanes

This project is to arrange the implementation of bus priority lanes in four areas.  More information has now been obtained from Wellington City Council, which will allow the investigations to proceed.

4.3	Karori Wildlife Sanctuary

Investigations are underway to resolve some issues relating to the operation of the two lakes by the Karori Wildlife Sanctuary Trust staff.

Laboratory Services

May 2000

Laboratory Services Department

Review of Operations for the Period Ended 31 May 2000

1.	Items of Note

- The Porirua City Council water testing contract is due for renegotiation and we will put a strong bid forward.

- Quality manuals have been revised in anticipation of IANZ’s visit later in the year.

- Procedures for the disposal of chemical waste have changed in accordance with the Environmental Policy.  Chemical Waste Company will remove chemical waste from the premises.

2.	Financial

The operating surplus is below budget at this stage.  Although operating expenditure is slightly under budget currently, the reduced level of internal revenue significantly outweighs any direct cost savings.

3.	Business Summary

3.1	Quality

There were no requests for retesting samples and test reports are being sent out within the agreed time frames.

3.2	Health and Safety

There are no incidents to report.

Plantation Forestry

May 2000

Plantation Forestry Department

Review of Operations for the Period Ended 31 May 2000

1.	Log Harvest Contract

May produced an income of $132,000 from an output of 4,059 tonnes.  This is a good result for the first “winter” month with significant rain.  One of the logging crews converted from ground based logging to hauler logging, which slowed production while they became familiar with the new equipment.

Recent grade outputs have been:

| Grade |  | Tonnes | % |
| --- | --- | --- | --- |
| Pruned Domestic |  | 0 | 0 |
| Pruned Export |  | 0 | 0 |
| Partial Pruned |  | 0 | 0 |
| S Grade |  | 954.9 | 23.5 |
| A Grade |  | 350.9 | 8.6 |
| L Grade |  | 462.5 | 11.4 |
| R Grade | (Renalls) | 151.2 | 3.7 |
| Rough | (Renalls) | 45.5 | 1.1 |
| K Sawlog |  | 414.3 | 10.2 |
| K Rough |  | 397.4 | 9.8 |
| Pulp |  | 1,006.6 | 24.8 |
| O/S Pulp |  | 102.9 | 2.5 |
| Other (Corsican) |  | 173.5 | 4.3 |
|  |  | 7,168.74 |  |

Prices have remained fairly static, with any currency gains being absorbed with increased shipping costs.  If the present upward trend in fuel prices continues, we can expect pressure from the trucking companies for compensation.

Renalls have now commenced sawing with their new mill.  This is attracting logs from both pulp and 58K grades at prices that offer a generous premium and thus represent far better value from our perspective.

Mitchpine have returned and are harvesting remnant stands of Corsican in Pakuratahi West, prior to moving into the larger stands in Pakuratahi East.  Given that winter is upon us, it is unlikely that they will be able to continue for long before the weather will drive them out.  Unfortunately there is little competition for this product and we are not in a position to dictate to the purchasers.  We can only hope that they return in the summer.

2.	Silviculture Contracts

Two hundred and fifty-nine hectares of a total 306 hectares of the current year’s contract have been completed.  Skilled Silviculture, which held the contract for the Mangaroa Block, has been advised that their contract has lapsed and they have removed all their equipment from the block.  The remainder of the block (32 ha) will be reallocated to another contractor.

Tenders have been sought for the 2000/01 silviculture programme.  These cover activities on 516 ha and close on 23 June.

3.	Plantation Forestry Operations

A quotation has been received for the supply and application of the fertiliser recommended by the Forest Research Institute following the recent foliage analysis.  The total cost is in excess of $70,000 so the proposal is being reviewed to either spread the application over two years or to reduce the costs to a more acceptable level.

The “fly by” part of the forest health survey was carried out late in the month.  If any suspect areas were detected, these will be inspected on foot.  We anticipate receiving a full report later in the year.

4.	Forest Access

Maungakotukutuku remains the only access problem but this is not serious as no work is programmed in the near future.

The new road into Pakuratahi East continues to be satisfactory, with no major problems.  Staff and contractors have carried out a “walk through” and agreed the remedial maintenance required before winter proper arrives.  This is being delayed by a lack of road graders in the area.  A close watch is being kept and should the condition of the road deteriorate we will insist that a grader be bought in to carry out the work.

There have been minor grade issues within the forest but the Contractor has addressed these at no cost, as they were not to agreed specification.

The Rallywoods’ agreement is now signed and the Contract for the construction of the bridge awarded to Works Infrastructure Ltd.  Work on-site is expected to commence on 3 July 2000.  We have also arranged an amendment to the resource consent for the construction of the bridge to permit work to continue through winter.

5.	Market Trends

Export markets remain static, with revenue gains being offset by shipping cost increases.  Demand remains buoyant, with increased demand anticipated from the new mill at Renalls in Waingawa.  They will prove a real boon while logging continues at Pakuratahi as they take logs that would otherwise be K58 or pulp grade.

A consequence of this is our intention to review the decision not to harvest Block 14/1.  This block consists of light stocking with relatively small trees, many of which would not meet the "small end diameter" specification for export and would have been downgraded to pulp.  A calculation including the new “Renall” specifications in the cutting programme produces a net return of $239,000 before roading costs.

# Text boxes

Error! Not a valid link.

Error! Not a valid link.